## Slide 1: Chapter 3 Basys3 and Arty FPGA Boards

## Slide 2: Outline
Introduction
The Basys3 Board
  Powering the Board
  Input/Output
  Configuring the FPGA
  Advanced Connectors
  External Memory
  Oscillator/Clock
The Arty Board
  Powering the Board
  Input/Output
  Configuring the FPGA
  Advanced Connectors
  External Memory
  Oscillator/Clock

## Slide 3: Introduction
We will use two different FPGA boards as Basys3 and Arty.
Both boards have Xilinx Artix-7 FPGA on them.
Basys3 is more suitable for education purposes since it has several input/output connections.
Arty is primarily developed for soft-core microcontrollers. Moreover, it has Arduino compatible pins. Hence, shields available for Arduino can be used with Arty.

## Slide 4: The Basys3 Board
Label Explanation
1 Power LED
2 Three Pmod connectors
3 Analog signal Pmod connector
4 Four-digit seven-segment display
5 Sixteen slide switches
6 Sixteen LEDs
7 Five push buttons
8 FPGA programming done LED
9 FPGA configuration reset button
10 Programmingmode jumper
11 USB host connector
12 VGA connector
13 Shared UART/JTAG USB port
14 External power connector
15 Power switch
16 Power source select jumper
17 Artix-7 FPGA
18 USB-UART bridge
19 Auxiliary function microcontroller
B1 SPI flash
B2 Power supply regulator
B3 Oscillator/clock

## Slide 5: The Basys3 Board
The Basys3 board can be powered either from the USB port or from an external power supply which should be connected to the external power connector. If an external power supply is used, it should be able to deliver a DC voltage between 4.5 V to 5.5 V with at least 1 A current.
Powering the Board
There are several digital input/output connections on the Basys3 board. These
can be summarized as peripheral module (Pmod) connectors, four-digit
seven-segment display, 16 slide switches, 16 LEDs, and five push buttons.
Input/Output
The Basys3 board Pmod connector pin layout.

## Slide 6: The Basys3 Board
The FPGA should be configured (programmed) in order to operate.
The configuration file will be generated by Vivado design suite.
The generated file can be fed to the FPGA in three ways.
  The first method is using the shared UART/JTAG USB port. We will use this method while configuring the FPGA through Vivado.
  The second method is using the SPI flash. To do so, the configuration file should have been stored in flash beforehand.
  The third method is storing the configuration file in a USB stick and using it through the USB host connector. By the help of an auxiliary function microcontroller, programming can be done.
Configuring the FPGA
There are advanced connectors on the Basys3 board. These are the USB host connector, VGA connector, and shared UART/JTAG USB port.
Advanced Connectors

## Slide 7: The Basys3 Board
The Basys3 board has a 32Mbit non-volatile serial flash as external memory. This device is connected to Artix-7 FPGA through a dedicated SPI bus. FPGA configuration files can be saved in this flash memory.
External Memory
The Basys3 board has an onboard oscillator/clock circuitry working at 100 MHz. The clock signal generated by the oscillator is fed to Artix-7 FPGA through its pins. Therefore, this onboard oscillator allows user to generate a required clock (within limits) in the design.
Oscillator/Clock

## Slide 8: The Arty Board
Label Explanation
1 FPGA programming done LED
2 Shared UART/JTAG USB port
3 Ethernet connector
4 Power source select jumper
5 Power jack
6 Power LED
7 Eight LEDs
8 Four slide switches
9 Four push buttons
10 Arduino/chipKIT shield connectors
11 SPI header (Arduino/chipKIT compatible)
12 chipKIT processor reset jumper
13 Programmingmode jumper
14 chipKIT processor reset button
15 Four Pmod connectors
16 FPGA configuration reset button
17 SPI flash
18 Artix-7 FPGA
19 DDR3 memory
20 Power supply regulator
21 USB-UART bridge
22 Ethernet transceiver
B1 Oscillator/clock

## Slide 9: The Arty Board
The Arty board can be powered in three ways as using the shared UART/JTAG USB port, external power jack, and Arduino/chipKIT connectors. We will use the shared UART/JTAG USB port is used for powering the board.
Powering the Board
There are several digital input/output connections on the Arty board. These can be summarized as four Pmod connectors, Arduino/chipKIT shield connector, four tri-color LEDs, four LEDs, four slide switches, four push buttons, and chipKIT processor reset button and jumper.
Input/Output

## Slide 10: The Arty Board
Configuring the FPGA on the Arty board is similar to Basys3.
Configuring the FPGA
There are advanced connectors on the Arty board. These are the shared UART/JTAG USB port, ethernet connector, and Arduino/chipKIT compatible SPI header.
Advanced Connectors
Arty has two different external memory blocks.
  The first one is a 128Mbit nonvolatile serial flash memory. This device is connected to Artix-7 FPGA through a dedicated SPI bus. FPGA configuration files can be saved in this flash memory.
  The second memory block on the Arty board is a 256MB DDR3L SDRAM.
External Memory

## Slide 11: The Arty Board
The Arty board has an onboard oscillator/clock circuitry working at 100 MHz.
Clock signal generated by the oscillator is fed to the Artix-7 FPGA through its pins. Therefore, this onboard oscillator allows user to generate a required clock (within limits) in the design.
Oscillator/Clock